## Slide 1
TrustMark: Universal Watermarking for Arbitrary Resolution Images
Summary of the research paper by Tu Bui, Shruti Agarwal, and John Collomosse.
Prepared by: [Your Name]
by PAVAN ARAVAPALLI

## Slide 2
Core Contributions
Novel Architecture
GAN-based model with frequency-aware loss for imperceptible watermarking.
Resolution Scaling
Supports watermarking images of any resolution via residual inference.
Watermark Removal Network
TrustMark-RM enables removal and re-watermarking of images.
State-of-the-Art Performance
Outperforms prior work in fidelity, robustness, and flexibility.

## Slide 3
TrustMark Architecture Overview
Embedder (E)
Embeds watermark into the image.
Noise Module (N)
Simulates real-world image degradations.
Extractor (X)
Recovers watermark from distorted images.

## Slide 4
Embedder: Watermark Injection
Input: Image (256×256×3) and binary watermark.
Uses MUNIT-style network to fuse watermark into image features.
Output: Watermarked image.
Input
Image and binary watermark data.
Process
Interpolation and fusion via deep network layers.
Output
Watermarked image ready for use.

## Slide 5
Extractor & Noise Module
Extractor (X)
ResNet-50 with sigmoid output recovers watermark.
Noise Module (N)
Geometric: crop, flip, resize
Photometric: JPEG, blur, brightness, contrast, Gaussian noise
Training Flow
End-to-end learning with differentiable perturbations.

## Slide 6
Joint Training Loss Functions
Total loss balances quality and watermark recovery accuracy.
Quality Loss
YUV, LPIPS, FFL, GAN+GP components
Recovery Loss
Binary Cross Entropy for watermark accuracy.

## Slide 7
TrustMark-RM: Watermark Removal
Architecture
Based on KBNet with denoising and attention mechanisms.
Function
Removes watermark while preserving image realism.
Losses
Decoder Consistency
Adversarial Loss
MSE Loss

## Slide 8
Resolution Scaling
Model trained at 256×256 but generalizes to any size using residuals.
Step 1
Resize image to 256×256.
Step 2
Apply TrustMark and compute residual.
Step 3
Upsample residual and apply to original image.

## Slide 9
Final Output and Inference
Output is clamped sum of original image and interpolated residual.
Plug-and-play method works at inference time for any resolution.
Flexible
Supports arbitrary image resolutions.
Efficient
No retraining needed for different sizes.

## Slide 10
Summary and Key Takeaways
Innovative Model
GAN-based watermarking with frequency-aware loss.
Versatile Scaling
Works on any image resolution via residuals.
Watermark Removal
TrustMark-RM removes watermarks preserving realism.
State-of-the-Art
Outperforms prior methods in fidelity and robustness.